WRFV3.7.1_LHN User guide

# Overview

The LHN assimilates instantaneous rainrate observations, in mm/hr. The observation are introduced into WRF through the auxiliary input channels. The accepted file input formats and the structure is the same as the WRF output files.
Therefore, the observations file should have the same grid as the WRF one.

NESTED DOMAINS AND MPI NOT SUPPORTED YET!!

Two variables are used by the LHN from the input file:
- RAINRATE_OBSERVATIONS(time, lat, lon)
  - Rainrate observations in mm/hr
- OBSERVATIONS_QUALITY(time, lat, lon)
  - Observations quality mask. All observations with a quality value greater than zero are processed.

# Namelist Control
The LHN data assimilation is controlled trought the namelist file. These are the options:Comien
namelist entry	section	type	defaul value	Description
auxinput6_inname	time_control	string	"auxinput6_d<domain>_<date>"	Observations input file name
auxinput6_interval_s	time_control	integer	0	Observations interval in seconds
io_form_auxinput6	time_control	integer	0	0=No input / 1=Grib / 2=Netcdf
lhn_type	latent_heat_nudging	integer	0	0=No LHN / 1=LHN
lhn_start	latent_heat_nudging	integer	0	LHN start time in seconds from the beggining of the simulation
lhn_end	latent_heat_nudging	integer	0	LHN end time in seconds from the beggining of the simulation
search_range	latent_heat_nudging	integer	10	Profile search radius [in grid points]
lhn_smooth_filter_sigma	latent_heat_nudging	float	1.0	Gaussian filter standard deviation [in grid points]
minimum_profile_scaling	latent_heat_nudging	float	0.333	Minimum profile scaling allowed
maximum_profile_scaling	latent_heat_nudging	float	2.0	Maximum profile scaling allowed
lhn_limit	latent_heat_nudging	float	0.0005	Latent heat nudging limit [K/s]